Dipolar optical plasmon in thin-film Weyl semimetals

Debasmita Giri1, Dibya Kanti Mukherjee2, Sonu Verma1, H. A. Fertig3,4, Arijit Kundu1

1Department of Physics, Indian Institute of Technology Kanpur, Kanpur 208016, India

2Laboratoire de Physique des Solides, CNRS UMR 8502, Universitè Paris-Saclay, 91405 Orsay Cedex, France

3Department of Physics, Indiana University, Bloomington, Indiana 47405, USA

4Quantum Science and Engineering Center, Indiana University, Bloomington, Indiana 47408, USA

In a slab geometry with large surface-to-bulk ratio, topological surface states such as Fermi arcs for Weyl or Dirac semimetals may dominate their low-energy properties. We investigate the collective charge oscillations in such systems, finding striking differences between Weyl and conventional electronic systems. Our results, obtained analytically and verified numerically, predict that time-reversal symmetry-broken Weyl semimetal thin films will host a single  ω ~ √q  plasmon mode that results from collective, antisymmetric charge oscillations between the two surfaces, in stark contrast to conventional 2D bilayers as well as Dirac semimetals with Fermi arcs, which support antisymmetric acoustic modes along with a symmetric optical mode. These modes lie in the gap of the particle-hole continuum and are thus spectroscopically observable and potentially useful in plasmonic applications.